## Slide 1: Abstractions
Sayan Mitra
Verifying cyberphysical systems
mitras@illinois.edu

## Slide 2: Review. Region automaton
Given an ITA , we construct the corresponding Region Automaton such that (i) visits the same set of locations (but does not have timing information) and (ii) is finite state machine.
ITA (clock constants) defines a set of clock regions, say . The set of states
is the set of states contain initial set of
We add the transitions between (regions)
  Time successors: Consider two clock regions , we say that is a time successor of if there exits a trajectory of ITA starting from that ends in ’
  Discrete transitions: Same as the ITA
Theorem. A location of ITA is reachable iff it is also reachable in
(we say that is time abstract bisimilar to )

## Slide 3
|X|! 2|X|
Corresponding FA
Drastically increasing with the number of clocks

## Slide 4: Later we will study how far the idea of abstractions can help analyze a hierarchy of Hybrid Automata
Nonlinear Hybrid
Automata
Integral Timed Automata
Rational Timed Automata
Multirate Automata
Rectangular Hybrid Automata
Rectangular Initialized Hybrid Automata

## Slide 5: Outline
Abstractions
Simulation relations
Composition and substitutivity

## Slide 6: Abstractions and Simulations
Consider models that have the same external interface (input/output variables and actions)
We would like to approximate one (hybrid) automaton with another one
We can over-approximate the reachable states of with those of
This would ensure that invariants of carry over to
We would like to go beyond invariants, and want to have more general requirements (e.g., CTL) carry over
should be simpler (smaller description, fewer states, transitions, linear dynamics, etc.) and preserve some properties of (and not others)
Verifying some requirements of can then carry over requirements to

## Slide 7: Finite state examples
A0
A1
0
1
1
0
A2
A3
0
1
B02
B13
0
1
C03
0,1
TracesB= 01*
TracesC= {0,1}*
A
B
C
An execution of A is
Trace is the visible or observable part of an execution
Set of all traces of

## Slide 8: Finite state examples
A0
A1
0
1
1
0
A2
A3
0
1
B02
B13
0
1
C03
0,1
B simulates A and vice versa.
A and B are bisimilar.
C simulates both A and B.
C is an abstraction of both A and B.
A
B
C

## Slide 9: How to prove B simulates A?
Show there exists a simulation relation from states of A to states of B. Say,
Show that for every transition and there exists such that
A0
A1
0
1
1
0
A2
A3
0
1
A
B02
B13
0
1
B

## Slide 10: Forward simulation relation
Consider a pair of automat and
Recall trace of an execution preserves the visible part of an execution
Definition. A relation is a forward simulation relation from to if
For every there exists a such that
For every transition and there exists such that
Theorem. If there exists a forward simulation from to then

## Slide 11
Theorem. If there exists a forward simulation from to then
Proof.
Consider any trace of There must exist a corresponding execution such that
We inductively construct a corresponding execution of such that
such that and [by start condition]
Suppose we have already constructed prefix of length ending in and such that and the traces corresponding to the prefixes are equal.
For any such that there exists
such that and
[by step condition]

## Slide 12: Finite state examples
A0
A1
0
1
1
0
A2
A3
0
1
B02
B13
0
1
C03
1
Check that A also simulates B and that C simulates both A and B.
Therefore, TracesA = TracesB
Does A simulate C?
A
B
C
0

## Slide 13: A Simulation Example
is an implementation of
Is there a forward simulation from to ?
Consider the forward simulation relation
24 cannot be simulated by from 2’ although (2,2’) are related.
1
2’
3
4
a
b
c
1
2
3
4
a
b
c
2
a

## Slide 14: Simulations for hybrid systems
Forward simulation relation from 1 to 2 is a relation R such that
  For every x1 ∈ there exists x2 ∈ such that x1 R x2
  For every x1 x1’ ∈ and x2 such that x1 R x2, there exists x2’ such that
    x2 x2’ and
    x1’ R x2’
  For every ∈ andx2 such that R x2, there exists that
    x2 = and
    x1’ R
Theorem. If there exists a forward simulation relation from hybrid automaton 1 to then for every execution of 1 there exists a corresponding execution of

## Slide 15: Simulation relations for hybrid automata
Recall condition 3 in definition of simulation relation:
Hybrid automata have transitions and trajectories
Different types of simulation depending on different notions for “Trace”
  Match for all variable values, action names, and time duration of trajectories (abstraction)
  Match variables but not time (time abstract simulation)
  Match a subset (external) of variables and actions (trace inclusion)
  Match single action/trajectory of A with a sequence of actions and trajectories of B

## Slide 16: Timer simulates Ball (w.r.t. timing of bounce actions)
Automaton Ball(c,v0,g)
variables:
x: Reals := 0
v: Reals := v0
actions: bounce
transitions:
bounce
pre x = 0 /\ v < 0
eff v := -cv
trajectories:
evolve d(x) = v; d(v) = -g
invariant
Automaton Timer(c, v0, g)
variables: analog
timer: Reals := ,
n:Naturals=0;
actions: bounce
transitions:
bounce
pre timer = 0
eff n:=n+1; timer :=
trajectories:
evolve d(timer) = -1
invariant timer

## Slide 17: Some nice properties of Forward Simulation
Let be comparable TAs. If R1 is a forward simulation from to and R2 is a forward simulation from to , then R1 R2 is a forward simulation from to
implements
The implementation relation is a preorder of the set of all (comparable) hybrid automata
  (A preorder is a reflexive and transitive relation)
If R is a forward simulation from to and R-1 is a forward simulation from to then R is called a bisimulation and are bisimilar
Bisimilarity is an equivalence relation
  (reflexive, transitive, and symmetric)
Notes: Relational composition

## Slide 18: Remark on Simulations and Stability
Stability not preserved by ordinary simulations and bisimulations [Prabhakar, et. al 15]
time
time
Stability Preserving Simulations and Bisimulations for Hybrid Systems, Prabhakar, Dullerud, Viswanathan IEEE Trans. Automatic Control 2015

## Slide 19: Backward Simulations
Backward simulation relation from 1 to 2 is a relation R such that
  If x1 ∈ and x1 R x2 then x2 ∈ such that
  If x’1 R x’2 and x1—a x1’ then
    x2 – x2’ and
    x1 R x2
    Trace() = a1
  For every ∈ andx2 ∈ such that x1’ R x2’, there exists x2 such that
    x2 – x2’ and
    x1 R x2
    Trace() =
Theorem. If there exists a backward simulation relation from 1 to then ClosedTraces1 ClosedTraces2
Notes: skip this maybe

## Slide 20: Abstractions II

## Slide 21: Abstraction recap
Defined what it means for to be abstraction of
If and then
Transitive, defines a preordering on compatible automata
We saw methods for proving
  Forward simulation and backward simulation
defines a preorder

## Slide 22: Outline
Abstractions and composition
CEGAR

## Slide 23: Substituting an automaton with its abstraction
Concrete system
Plant
Controller

## Slide 24: Substituting an automaton with its abstraction
Abstract system
Plant
Controller
Abstract Controller

## Slide 25: How is the abstract system related to the concrete system?
Controller
Abstract system
Plant
Abstract Controller
Concrete system
Plant
Controller
Abstract Controller
Does
imply
?

## Slide 26: Hybrid IO Automaton
Recall a hybrid automaton
We will partition the set of variables of into
  : internal or state variables (do not interact)
  : output variables
  : input variables
This gives rise to hybrid I/O automata (HIOA)
[Lynch, Segala, Vaandrager 2002]
We define composition of compatible HA
Plant
Controller

## Slide 27: Composition of Hybrid Automata
The parallel composition operation on automata enable us to construct larger and more complex models from simpler automata modules
1 to 2 are compatible if X1 ∩ X2 = H1 ∩ A2 = H2 ∩ A1 = ∅
Variable names are disjoint; Action names of one are disjoint with the internal action names of the other

## Slide 28: Composition
For compatible 1 and 2 their composition 1 || 2 is the structure =
Variables
  , ,
Actions
  , ,
iff for
  and )
: set of trajectories for V
  𝜏 iff , i

## Slide 29
e
f
a1
a1
a1
a1
u2
e
f
u2

## Slide 30: Modeling a Simple Failure Detector System
Periodic send
Channel
Timeout
Send
Channel
Failure Detector
Send(m)
recv(m)
fail
detect

## Slide 31: Composition
For compatible 1 and 2 their composition 1 || 2 is the structure =
(disjoint union)
H = H1 ∪ H2 (disjoint union)
E = E1 ∪ E2 and A= E ∪ H
iff
  and ) 1 and
  and ) 2 and
  Else, ) 1 and ) 2
: set of trajectories for X
  𝜏 iff , 𝜏.Xi i
Theorem . is also a hybrid automaton.

## Slide 32: Example: Send || TimedChannel
Automaton PeriodicSend(u, M)
variables: internal clock: Reals := 0
actions: external send(m:M)
transitions:
send(m)
pre clock = u
eff clock := 0
trajectories:
evolve d(clock) = 1
stop when clock=u
Automaton Channel(b,M)
variables: internal
queue: Queue[M,Reals] := {}
clock1: Reals := 0
actions: external send(m:M), receive(m:M)
transitions:
send(m)
pre true
eff queue := append(<m, clock1+b>, queue)
receive(m)
pre head(queue)[1] = m
eff queue := queue.tail
trajectories:
evolve d(clock1) = 1
stop when ∃ m, d, <m,d> ∈ queue
/\ clock=d

## Slide 33: Composed Automaton
Automaton SC(b,u)
variables: internal queue: Queue[M,Reals] := {}
clock_s, clock_c: Reals := 0
actions: external send(m:M), receive(m:M)
transitions:
send(m)
pre clock_s = u
eff queue := append(<m, clock_c+b>, queue); clock_s := 0
receive(m)
pre head(queue)[1] = m
eff queue := queue.tail
trajectories:
evolve d(clock_c) = 1; d(clock_s) = 1
stop when
(∃ m, d, <m,d> ∈ queue /\ clock_c=d)
\/ (clock_s=u)

## Slide 34: Modeling a Simple Failure Detector System
Periodic send || Channel
Periodic send || Channel || Timeout
Send
Channel
Failure Detector
Send(m)
recv(m)
fail
detect

## Slide 35: Time bounded channel & Simple Failure Detector
Automaton Timeout(u,M)
variables: internal suspected: Boolean := F,
clock: Reals := 0
actions: external receive(m:M), timeout
transitions:
receive(m)
pre true
eff clock := 0; suspected := false;
timeout
pre ~suspected /\ clock = u
eff suspected := true
trajectories:
evolve d(clock) = 1
stop when clock = u /\ ~suspected

## Slide 36: General composition

## Slide 37: Time bounded channel & Simple Failure Detector
Automaton Timeout(u,M)
variables: suspected: Boolean := F,
clock: Reals := 0
actions: external receive(m:M), timeout
transitions:
receive(m)
pre true
eff clock := 0; suspected := false;
timeout
pre ~suspected /\ clock = u
eff suspected := true
trajectories:
evolve d(clock) = 1
stop when clock = u /\ ~suspected
Automaton Channel(b,M)
variables: queue: Queue[M,Reals] := {}
clock: Reals := 0
actions: external send(m:M), receive(m:M)
transitions:
send(m)
pre true
eff queue := append(<m, clock+b>, queue)
receive(m)
pre head(queue)[1] = m
eff queue := queue.tail
trajectories:
evolve d(clock) = 1
stop when ∃ m, d, <m,d> ∈ queue
/\ clock=d

## Slide 38: Some properties about composed automata
L= 1 || 2 and let α be an execution fragment of
  Then αi = α|(Ai, Xi) is an execution fragment of i
  α is time-bounded iff both α1 and α2 are time-bounded
  α is admissible iff both α1 and α2 are admissible
  α is closed iff both α1 and α2 are closed
  α is non-Zeno iff both α1 and α2 are non-Zeno
  α is an execution iff both α1 and α2 are executions
Traces | Ei ϵ Traces i }
See examples in the TIOA monograph

## Slide 39: A trace theorem restriction from composition of I/O automata
Theorem 5.5 (from Theory of Timed I/O Automata by Lynch et. al.)
Suppose 1||2 and let E be the set of input/output actions of A. Then is exactly the set of (E, ∅)-sequences whose restrictions to 1 and 2 are traces of 1 2 , respectively. That is,
= {β | β is an (E, ∅)-sequence and ∈ , i ∈ {1, 2}}.

## Slide 40: Substitutivity
Theorem 1. Suppose 1 , 2 and have the same external interface and 1 , 2 are compatible with . If 2 then 1|| 2 ||

## Slide 41: Substutivity
Theorem 2. Suppose 1 2 and 2 are HAs and 1 2 have the same external actions and 2 have the same external actions and 1 2 is compatible with each of1 and 2 .
If 1 and 2 then 1 2||2 .
Proof. 1 2||
  2|| 2||
  By transitivity of implementation relation
  1 2||

## Slide 42: A stronger substitutivity result
Theorem 3. 1 2||2 and then 1 2||2.

## Slide 43: A stronger substitutivity result
Theorem 3. 1 2||2 and
then 1 2||2.
Proof. Let β ∈ .
By Theorem 5.5 (of LVS TIOA), and .
Since
By Theorem 5.5 , β ∈
Since 1 2||2 by assumption, β ∈

## Slide 44: Counter-example guided abstraction-refinement

## Slide 45: Counterexample guided abstraction refinement (CEGAR)
A general algorithmic framework for automatically constructing and verifying property-specific abstractions [Clarke:2000]
CEGAR has been applied to discrete automata, software, and hybrid systems [Holzman 00,Ball 01, Alur 2006,Clarke 2003, Fehnker2005, Prabhakar 15, Roohi 17]
We will discuss the basic idea of the CEGAR and the key design choices, and their implications.

## Slide 46
Start with coarse abstraction B0
Check Bi satisfies S ?
 counter-example for A?
Refine Bi to get Bi+1
 = q0 q1 q2 … qn
A is safe
Yes
No
A unsafe
Yes
No
Idea of CEGAR

## Slide 47: Key design choices
Space of the abstract automata (finite, timed, linear)
Model checker for abstract automaton
Counter-example validation procedure
Refinement strategy