## Slide 1: Modeling Cyberphysical Systems
Sayan Mitra
Verifying cyberphysical systems
mitras@illinois.edu

## Slide 2: Outline
Modeling cyber-physical systems
  Hybrid automata
  Executions
  Urgency
Zeno
Hybrid stability

## Slide 3: Why combine discrete and continuous time models?
Engineering systems can have dynamics with widely different time constants
  Software for AV updates at 1 GHz --- human scale motion 10 Hz
  Electrical circuit breakers 50 Hz --- power system dynamics 0.1 – 1 Hz
Widely different time constants can make computation numerically unstable
Some state changes are naturally described by automata:
  programs, automata, SMT, switching rules, etc.
while others are naturally described by ODEs:
  motion of planets and satellites, physical laws, weather

## Slide 4: Example. Thermostat automaton
automaton Thermostat(u, l, K, h : Real) where u > l
type Status enumeration [on, off ] actions
turnOn; turnOff;
variables
x: Real := l loc: Status := on
transitions
turnOn
pre x≤l ∧ loc=off
eff loc := on
trajectories
modeOn
evolve d(x) = K(h − x)
invariant loc = on ∧ x ≤ u
turnOff
pre x≥u ∧ loc=on
eff loc := off
modeOff
evolve d(x) = −Kx
invariant loc = off ∧ x ≥ l
Determinism vs nondeterminism
mode invariants

## Slide 5: Recall language for automata
An automaton tuple
is a set of variables; each is associated with a type,
  A valuation for maps each variable in X to its type
  Set of all valuations: is the state space
set of initial or start states
is a set of names of actions or labels
is the set of transitions
  a transition is a triple
  defined by pre and eff
  We write it as
automaton DijkstraTR(N:Nat, K:Nat), where K > N
type ID: enumeration [0,...,N-1]
type Val: enumeration [0,...,K]
actions
update(i:ID)
variables
x:[ID -> Val]
transitions
update(i:ID)
pre i = 0 /\ x[i] = x[N-1]
eff x[i] := (x[i] + 1) % K
update(i:ID)
pre i >0 /\ x[i] ~= x[i-1]
eff x[i] := x[i-1]

## Slide 6: Trajectories
For set of variables and time interval of the form , a trajectory for is a function
We will specify as solutions of differential equations
first state of
If is right closed then the limit state of
If is finite then duration of is
Domain of
A point trajectory is a trajectory with
A prefix of , is a function such that and for all

## Slide 7: Hybrid Automaton
=
: set of state variables
  set of states
set of start states
set of actions, A= E ∪ H
: set of trajectories for X which is closed under prefix, suffix, and concatenation
Notes: Pick a couple of nice examples

## Slide 8: Semantics: Executions and Traces
An execution of is an (possibly infinite) alternating sequence where
  ∀ i,
  If .fstate ∈ then is an execution
Execs set of all executions
First state of is
If is finite and closed then
A state is reachable if there exists an execution with
turnOn
turnOn
turnOn
turnOff
turnOff

## Slide 9: Mode invariants: Urgency in transitions
The trajectories in a hybrid automaton are often specified as solutions of ODEs
Solutions of ODEs define a family of trajectories which are closed under prefix, suffix, and concatenation
Nothing prevents a trajectory to continue forever unless an action is forced to occur by a mode invariant
turnOn
turnOn
turnOn
turnOff
turnOff

## Slide 10: Example. Bouncing Ball
automaton Bouncingball(c,h,g)
variables: x: Reals := h, v: Reals := 0
actions: bounce
transitions:
bounce
pre x = 0 /\ v < 0
eff v := -cv
trajectories:
Loc1
evolve d(x) = v; d(v) = -g
invariant
Loc 1
Graphical Representation used in many articles
bounce
x = 0 /\ v < 0
v’ := -cv
x:= h
mode invariant, not to be confused with invariants of the automaton
Notes: Guard, Precondition
Effect, Reset map
Invariance

## Slide 11: Urgency: Must transitions
automaton Thermostat(u, l, K, h,d : Real) where u > l
type Status enumeration [on, off ] actions
turnOn; turnOff;
variables
x: Real := l loc: Status := on
transitions
turnOn
pre x≤l ∧ loc=off
eff loc := on
trajectories
modeOn
evolve d(x) = K(h − x)
invariant loc = on ∧ x ≤ u + d
turnOff
pre x≥u ∧ loc=on
eff loc := off
modeOff
evolve d(x) = −Kx
invariant loc = off ∧ x ≥ l - d
An urgent transition (or action) is an action that has to occur as soon as it is enabled
Introduce special syntax for creating urgent transitions, but we can use mode invariants to accomplish this

## Slide 12: Another Example: Periodically Sending Process
Automaton PeriodicSend(u)
variables: analog
clock: Reals := 0, z:Reals, failed:Boolean := F
actions: send(m:Reals), fail
transitions:
send(m)
pre clock = u /\ m = z /\ ~failed
eff clock := 0
fail
pre true
eff failed := T
trajectories:
evolve d(clock) = 1, d(z) = f(z)
invariant failed \/ clock<=u
Loc 1
~failed
send(m)
clock = u /\ m = z /\ ~failed
clock := 0
clock:= 0
fail
true
failed := T

## Slide 13: Zeno’s Paradox
Achilles runs 10 times faster than than the tortoise, but the turtle gets to start 1 second earlier. Can Achilles ever catch Turtle?
Lesson: Mixing discrete transitions with continuous motion can be tricky!
Achilles, the fastest athlete, greatest warrior
Zeno, Greek philosopher
You couldn’t even beat a turtle
After 1/10th of a second, Achilles reaches where the Turtle (T) started, and T has a head start of 1/10th second.
After another 1/100th of a second, A catches up to where T was at t=1/10 sec, but T has a head start of 1/100th
…
T is always ahead …
whatever!
Notes: 5 mins.

## Slide 14: Defining stability of hybrid automata
Given an admissible execution
Recall, stability is defined in terms of ; two issues
We would like to view an execution as But, how to define ?
define where is the longest prefix of with
Also, has valuations of discrete variables (loc) and continuous variable (x): ignore discrete variable when discussing stability
Now, we can import all the definitions of Lyapunov stability and asymptotic stability from dynamical system models to hybrid automata
Question. How can we check stability of a hybrid automaton?
time

## Slide 15
Run
Walk
Each of the modes of a walking robot are asymptotically stable
Is it possible to switch between them to make the system unstable?
Stability of a hybrid automaton

## Slide 16
Run
Walk
Yes! By switching between them the system becomes unstable
Notes: So, 300 years of mathematics developed for analyzing physics will not be enough for analyzing systems like self-driving cars where computers switch between different physics

## Slide 17: Summary
Interesting features in hybrid models
Interaction between transitions, trajectories, and mode invariants can lead to extra sources of nondeterminism; transitions can be made urgent with mode invariants
Mode switches can make the system unstable
Zeno behavior
Inductive invariance proofs work with additional condition for trajectory closure
Trajectory closure can be checked with subtangential condition, Lyapunov functions, Barrier certificates