## Slide 1: Reachability analysis
Sayan Mitra
Verifying cyberphysical systems
mitras@illinois.edu

## Slide 2: Next few lectures
Focus on specific classes of hybrid automata for which safety properties (invariants) can be verified completely automatically
  Finite state machines
  Alur-Dill’s Timed Automata[1] (Today)
  Rectangular initializaed hybrid automata
  Linear hybrid automata
  …
We will introduce abstractions: Simplifying or approximating one automaton A with another automaton B
[1] Rajeev Alur et al. The Algorithmic Analysis ofHybrid Systems. Theoretical Computer Science, volume 138, pages 3-34, 1995.

## Slide 3: Today
Finite state machines
Algorithmic analysis of (Alur-Dill’s) Timed Automata[1]
  A restricted class of what we call hybrid automata in this course with only clock variables
[1] Rajeev Alur and David L. Dill. A theory of timed automata. Theoretical Computer Science, 126:183-235, 1994.

## Slide 4: Reachability of Finite Automata
An finite automaton is a tuple where
is a finite set of states
is the set of initial or start states
is the set of transitions
An execution of is an alternating sequence of states and actions such that:
  in the sequence,
A state is reachable if there exists an execution such that

## Slide 5: Reachability in finite state machines
set of states reachable from by automaton
An invariant is a set of states I such that
How to check whether is reachable ?
Q: All states e.g.
Invariant e.g.

## Slide 6: Reachability as graph search
Q1. Given is a state reachable?
Define a graph where
Q2. Does there exist a path in from any state in to
Perform Depth First or Breadth First Search on from
Time complexity of BFS
Space complexity is )

## Slide 7: Nondeterministic reachability
Input: G = (V, E)
vcurrent := choose
If vcurrent return ‘‘yes”
Else For i = 1 to :
vnext := choose V
If (vcurrent, vnext) E break
If vnext T return ‘‘yes”
vcurrent := vnext
Return ‘‘no”
Requires only O(log |Q|) bits of memory
Using Savitch’s construction we get a deterministic algorithm that uses O(log2|Q|) bits

## Slide 8: Adding Clocks and Clock Constraints
A clock variable x is a continuous (analog) variable of type real such that along any trajectory of x, for all t .
For a set X of clock variables, the set (X) of integral clock constraints are expressions defined by the syntax:
  g ::= x
  where
Examples: x = 10; x [2, 5); true are valid clock constraints
What do clock constraints look like?
Semantics of clock constraints

## Slide 9: Integral Timed Automata
Definition. A integral timed automaton is a HIOA where
  V = X , is a set of n clocks and is a discrete state variable of finite type ; stata space
  A is a finite set
  is a set of transitions such that
    The guards are described by clock constraings
    implies either or
  set of clock trajectories for the clock variables in X

## Slide 10: Example: Light switch
Math Formulation
automaton Switch
  variables
  internal x, y:Real := 0, loc: {on,off} := off
  transitions
  internal push
pre x 2
eff if loc = on then x := 0
else x,y := 0; loc := off
  internal pop
pre y = 15 /\ loc = off
eff x := 0
  trajectories
invariant loc = off => y 15
evolve d(x) = 1; d(y) = 1
Description
Switch can be turned on whenever at least 2 time units have elapsed since the last turn on. Switches off automatically 15 time units after the last on.

## Slide 11: Timed Automaton application in Web Services (WS)
Modelling and Verification of Web Services Business Activity Protocol Anders P. Ravn, Jiri Srba, and Saleem Vighio, RV 2010
WS-Coordination describes a framework for coordinating transactional web services
Network protocol described in state tables
600+ lines of C-like code in the protocol model
Modeled and Verified using the UPPAAL tool
Analysis considers different channel models
The main safety property: protocol does not enter invalid state
Property violated in all but the FIFO channel model

## Slide 12: Control State (mode) Reachability Problem
Given an ITA , check if a particular (mode) control state is reachable from the initial states
Why is mode reachability good enough even if we are interested in checking reachability of ?

## Slide 13: Model Reachability of Integral Timed Automata is Decidable [Alur Dill 94]
That is, there is an algorithm that takes in and terminates with the correct answer.
Key idea:
  Construct a finite automaton that is a time-abstract bisimilar to the given ITA
  That is, FA behaves identically to ITA w.r.t. control state reachability, but does not preserve timing information
  Check reachability of FA

## Slide 14: An equivalence relation with a finite quotient
Under what conditions do two states x1 and x2 of the automaton behave identically with respect to control state reachability (CSR)?
  When do they satisfy the same set of clock constraints?
  When would they continue to satisfy the same set of clock constraints?

## Slide 15: An equivalence relation with a finite quotient
Under what conditions do two states x1 and x2 of the automaton behave identically with respect to mode reachability ?
  When do they satisfy the same set of clock constraints?
  When would they continue to satisfy the same set of clock constraints?
x1.and
x1 and x2 satisfy the same set of clock constraints
  For each clock int(x1.) = int(x2.) or int(x1.and int(x2.. ( of )
  For each clock with x1., frac(x1.iff frac(x2.
  For any two clocks and with x1. and x1., frac(x1.) frac(x1.) iff frac(x2.) frac(x2.)
Lemma. This is an equivalence relation on val(V) the states of
The partition of val(V) induced by this relation is are called clock regions

## Slide 16: What do the clock regions look like?
Example of Two Clocks
X = {y,z}
= 2
= 3

## Slide 17: Complexity
Lemma. The number of clock regions is bounded by |L||X|! 2|X|.

## Slide 18: Region automaton
Given an ITA , we construct the corresponding Region Automaton
visits the same set of modes (but does not have timing information) and
is finite state machine.
ITA (clock constants) defines a set of clock regions, say . The set of states
is the set of states contain initial set of
We add the transitions between (regions)
  Time successors: Consider two clock regions , we say that is a time successor of if there exits a trajectory of ITA starting from that ends in ’
  Discrete transitions: Same as the ITA
Theorem. A mode of ITA is reachable iff it is also reachable in
(we say that is time abstract bisimilar to )

## Slide 19: Time successors
The clock regions in blue are time successors of the clock region in red.

## Slide 20: Example 1: Region Automata
ITA
Corresponding FA

## Slide 21: Example 2
ITA
Clock Regions

## Slide 22
|X|! 2|X|
Corresponding FA
Drastically increasing with the number of clocks

## Slide 23: Special Classes of Hybrid Automata
  Finite Automata
  Integral Timed Automata 
  Rational time automata
  Multirate automata
  Rectangular Initialized HA
  Rectangular HA
  Linear HA
  Nonlinear HA

## Slide 24: ACM NEWS: In Space, No One Can Fix Your Sign Errors--- Paul Cheng & Peter Carian
15,000 satellite launches planned for the decade
5.3% satellites are lost in the first year, 42% of those in first 2 months
Most common cause sign errors: SW/HW parameter used the wrong way
fitting acceleration sensors the wrong way
wrong usage of negative instead of positive parameters
switching current in wrong direction in a circuit
inverting the orientation of the electromagnets used for positioning
Genesis (2001) for capturing particles from the solar wind, pounded into the Utah desert unbraked because a pencil-eraser-sized deceleration sensor was mounted upside-down.

## Slide 25: Clocks and Rational Clock Constraints
A clock variable x is a continuous (analog) variable of type real such that along any trajectory of x, for all t .
For a set X of clock variables, the set (X) of rational clock constraints are expressions defined by the syntax:
  g ::= x
  where
Examples: x = 10.125; x [2.99, 5); true are valid rational clock constraints
Semantics of clock constraints

## Slide 26: Step 1. Rational Timed Automata
Definition. A rational timed automaton is a HA = where
  V = X , where is a set of n clocks and is a discrete state variable of finite type Ł
  A is a finite set
  is a set of transitions such that
    The guards are described by rational clock constraings
    implies either or
  set of clock trajectories for the clock variables in X

## Slide 27: Example: Rational Light switch
Switch can be turned on whenever at least 2.25 time units have elapsed since the last turn off or on. Switches off automatically 15.5 time units after the last on.
automaton Switch
internal push; pop
variables
internal x, y:Real := 0, loc:{on,off} := off
transitions
push
pre x >=2.25
eff if loc = on then y := 0 fi; x := 0; loc := off
pop
pre y = 15.5 loc = off
eff x := 0
trajectories
invariant loc = on loc = off
stop when y = 15.5 loc = off
evolve d(x) = 1; d(y) = 1

## Slide 28: Control State (Location) Reachability Problem
Given an RTA, check if a particular mode is reachable from the initial states
Is problem decidable?
Yes
Key idea:
  Construct a ITA that has exactly same mode reachability behavior as the given RTA (timing behavior may be different)
  Check mode reachability for ITA

## Slide 29: Construction of ITA from RTA
Multiply all rational constants by a factor q that make them integral
Make d(x) = q for all the clocks
RTA Switch reaches the same control locations as the ITA Iswitch
Simulation relation R is given by
(u,s) iff u.x = 4 s.x and u.y = 4 s.y
automaton ISwitch
internal push; pop
variables
internal x, y:Real := 0, loc:{on,off} := off
transitions
push
pre x >= 9
eff if loc = on then y := 0 fi; x := 0; loc := off
pop
pre y = 62 loc = off
eff x := 0
trajectories
invariant loc = on loc = off
stop when y = 62 loc = off
evolve d(x) = 4; d(y) = 4

## Slide 30: Step 2. Multi-Rate Automaton
Definition. A multirate automaton is = where
  V = X , where is a set of n continuous variables and is a discrete state variable of finite type Ł
  A is a finite set of actions
  is a set of transitions such that
    The guards are described by rational clock constraings
    implies either
  set of trajectories such that
  for each variable

## Slide 31: Control State (Location) Reachability Problem
Given an MRA, check if a particular location is reachable from the initial states
Is problem is decidable? Yes
Key idea:
  Construct a RTA that is bisimilar to the given MRA

## Slide 32: Example: Multi-rate to rational TA

## Slide 33: Step 3. Rectangular HA
Definition. A rectangular hybrid automaton (RHA) is a HA where
  V = X , where X is a set of n continuous variables and is a discrete state variable of finite type Ł
  A is a finite set
  set of trajectories for X
    For each either (i) or (ii)
    Equivalently, (i)
    (ii)
  is a set of transitions such that
    Guards are described by rational clock constraings
    implies

## Slide 34: CSR Decidable for RHA?
Given an RHA, check if a particular location is reachable from the initial states?
Is this problem decidable? No
  [Henz95] Thomas Henzinger, Peter Kopke, Anuj Puri, and Pravin Varaiya. What's Decidable About Hybrid Automata?. Journal of Computer and System Sciences, pages 373–382. ACM Press, 1995.
  CSR for RHA reduction to Halting problem for 2 counter machines
  Halting problem for 2CM known to be undecidable
  Reduction in next lecture

## Slide 35: Step 4. Initialized Rectangular HA
Definition. An initialized rectangular hybrid automaton (IRHA) is a RHA where
  V = X , where X is a set of n continuous variables and is a discrete state variable of finite type Ł
  A is a finite set
  set of trajectories for X
    For each either (i) or (ii)
    Equivalently, (i)
    (ii)
  is a set of transitions such that
    Guards are described by rational clock constraings
    implies if dynamics changes from to then , otherwise

## Slide 36: Example: Rectangular Initialized HA
1
2
3
Pre Eff
Both Pre have to be reset
Eff

## Slide 37: CSR Decidable for IRHA?
Given an IRHA, check if a particular location is reachable from the initial states
Is this problem decidable? Yes
Key idea:
  Construct a 2n-dimensional initialized multi-rate automaton that is bisimilar to the given IRHA
  Construct a ITA that is bisimilar to the Singular TA

## Slide 38: From IRHA to Singular HA conversion
For every variable create two variables---tracking the upper and lower bounds
IRHA | MRA
 | ;
Evolve: | Evolve: ;
Eff: | Eff:
Guard: | 
 | Eff
IRHA | MRA

## Slide 39: Example IRHA
v1
v2
v3
v4
2
2

## Slide 40: Initialized Singular HA
v1
v2
v3
v4

## Slide 41: Transitions
5
v1
-3
no reset
-3

## Slide 42: Initialized Singular HA
v1
v2
v3
v4
2
2
2

## Slide 43: Can this be further generalized ?
For initialized Rectangular HA, control state reachability is decidable
  Can we drop the initialization restriction?
    No, problem becomes undecidable (next time)
  Can we drop the rectangular restriction?
    No, problem becomes undecidable

## Slide 44: Practical reachability
Tools:
SpaceEX
CORA
C2E2
Flow*
DryVR

## Slide 45: Data structures critical for reachability
Hyperrectangles
Polyhedra
Zonotopes [Girard 2005]
Ellipsoids [Kurzhanskiy 2001]
Support functions [Guernic et al. 2009]
Generalized star set [Duggirala and Viswanathan 2018]

## Slide 46: Reachability in practice

## Slide 47
C2E2 generated safety certificate for a given user model
Unsafe region
Reach set
Verify no collision with uncertainties: speeds in [70, 85] mph and acceleration range of NPC

## Slide 48: For a different user model C2E2 finds a corner case
counter-example
visualized
Verify no collision with uncertainties like speeds in [70, 85] mph and bigger acceleration range of NPC
SAYAN MITRA @Mitrasayn

## Slide 49: Data structures: rectangles and ellipsoids

## Slide 50: Zonotopes and polytopes

## Slide 51: Takeaway messages
For restricted classes of HA, e.g., ITA, IRHA, Control state reachability is decidable (Alur-Dill)
The problem becomes undecidable for RHA (Henzinger et al.)
  Important message to re-focus on relaxed problem
  Bounded time, approximate reachability
Many tools and successful applications using iterative Post computations
Choice of data-structure critical for practical performance
Notes: fix-point implementation in tools
We can remove the init. set. Hytech will accept the automaton, but there is no guarantee on termination